## Slide 1
James Delaney & Hudson Bowen
Electronics 1: Guitar Pedal Project

## Slide 2
Inspiration/Background
-Originally, I was not going to do a project as I couldn’t think of anything I wanted to do.
-Looked over and saw my guitar, project idea!
-Hudson and I decided to make an overdrive pedal, which features soft clipping at peaks to achieve a slightly distorted tone using an op amp and other circuitry techniques we learned in class.

## Slide 3
Circuit Overview
Three distinct sections
DC and AC inputs
Feedback loop
Potentiometers and output

## Slide 4
Circuit Analysis
DC Bias Voltage
  DC Bias point achieved through voltage divider across R1 and R2
  C2 removes AC noise from battery
AC Signal
  C3 and R3 couple the AC and DC voltages
  C1 removes any AC voltage above R3 by acting as a short for AC signal
Thus, our non-inverting input voltage is 4.5 V plus the input AC signal

## Slide 5
Circuit Analysis
Setup as a modified Non-Inverting Amplifier
Only AC Signal is amplified
  C4 acts as an open circuit for DC signal, but a short for AC signal
When the diodes are off, the gain of the AC signal is:
However, when the output voltage’s magnitude is high enough, the diodes begin to conduct current
  When this occurs, the output voltage needed to provide R6 with enough current to keep the inverting input decreases
  This effectively lowers the gain of the amplifier, causing a “soft clip”

## Slide 6
Circuit Analysis

## Slide 7
Circuit Analysis

## Slide 8
Circuit Analysis
C6 behaves as a decoupling capacitor to isolate our signal
R7 and C7 behave as a low pass filter, allowing tone control
R8 controls output amplitude (volume)
  R8 needs to be much larger than R7 to better control volume
    Voltage divider across R7 and R8
Tone knob
Volume knob

## Slide 9
Practical Implementation

## Slide 10
Results - Volume Knob
High Resistance
Low Resistance
Yellow = output
Green = input
Top(1) = 160mV
Base(1) = -200mV
Top(1) = 400mV
Base(1) = -440mV

## Slide 11
Results - Tone Knob
High Resistance
Low Resistance
Yellow = output
Green = input
Smoother rise in tone when turned down

## Slide 12
Results - Gain Knob
Low Resistance
High Resistance
Yellow = output
Green = input
From clean tone to distorted, clipped tone

## Slide 13
Thank You!
Q&A